## Slide 1: RECAP OF LAST YEAR

## Slide 2: Car trajectory estimation
Recap of last year
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
Description
  Deep learning approach for predicting the car’s near future path (or trajectory), based on disparity images
    Predicts car’s movements over the next second, can be used for steering / braking
Architecture
  Deep learning network built from scratch based on state of the art techniques
Current status
  Part of OFT team, working of flow-based object detection (series production for FVG3)
  Still keeping an eye on deep learning topics
    Mentor for Road condition monitoring topic, which is needed for Motorcycle project(s)
    Pass on knowledge and expertise gained

## Slide 3: ROAD CONDITION MONITORING

## Slide 4: Overview
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
Description
  Deep learning approach for identifying the road condition: dry, wet, snow (possibly others as well later on)
  Typical classification task
  We can use the already available set of sequences from Bosch dataset

## Slide 5: Dataset
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
Dumped images from Bosch sequences
Labeled the entire sequence with the same class -> drawbacks
~75000 training images (25k from each class)
~15000 validation images (5k from each class)
~15000 test images (5k from each class)
102 dry sequences
62 wet sequences
18 snow sequences

## Slide 6: Literature study
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
  Network architecture based on state of the art techniques
    Deep convolutional network
    Parallel filters
    Residual addition
Deep convolutional neural network
Residual addition
Parallel filters

## Slide 7: Architecture
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
  Deep learning network built from scratch
  Work still in progress on different architectures
Residual & parallel model approach
Dedicated predictor approach
Simple, “classical” approach

## Slide 8: Evaluation – favourable scenarios
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
Expected: Dry
Dry – 98.06 %
Wet – 1.86 %
Snow – 0.08 %
Expected: Wet
Dry – 0.06 %
Wet – 99.89 %
Snow – 0.05 %
Expected: Snow
Dry – 0.49 %
Wet – 0.14 %
Snow – 99.36 %

## Slide 9: Evaluation – difficult scenarios
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
Expected: Wet
Dry - 71.75 %
Wet - 27.24 %
Snow - 1.02 %
Expected: Snow
Dry – 13.42 %
Wet – 56.99 %
Snow – 29.59 %
Accuracy evaluation:
  Validation set: 96.10%
  Test set: 86.62%
Prediction time evaluation
  ~10 fps
  Depends on the model used

## Slide 10: Future steps
Road condition monitoring
Automotive Electronics | RBRO/ESA1 | 2018-03-12
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
Train the network on a bigger dataset
Optimize the network
Implement in SIL
Reuse network structure for other tasks also:
  Context estimation